## Slide 1: Meshing Algorithm – Logical Workflow
User Input
End Zones
Last zone
Cell size from end of previous zone
Expansion vector
Cell size increases as specified by the expansion factor. Expands until cell reaches Maximum Cell Size or End of Zone
First zone
Cell size from second zone
Vector Solver
Inputs
Transition/Expansion factors
Transition/Expansion vectors
Overlapping cells
Overlapping Cell is moved down of one.
Check Transitions
Transition factor > 1.4
Or
Last Transition cell >=
Last expansion cell
Transition factor < 1.0
Or
Last expansion cell >=
Last Transition cell * 1.4
Add a cell
Transition factor is re-computed
Remove a cell
Transition factor is re-computed
Initialize vectors
Expansion vector is truncated at the Overlapping Cell
Compute new transition factor to fill the zone.
Output Zone Mesh
Pass
Fail
Center Zones
Compute vectors
  Compute expansion vector
  Compute transition vector from zone below
  Find best overlapping cells
Case 1
Zone below has smaller cell size
Best overlapping cells are larger than Maximum Cell Size allowed.
Replace large cells by Maximum Cell Size and re-compute vectors
Case 2
Zone below has larger cell size
Best overlapping cells occurs at the first cell of the zone
Set expansion to 1.0 and re-compute best overlapping cell
Expansion vector cannot match the cells from below (expansion factor = 1.0 )
Expansion vector fills the zone and the transition occurs in the next zone
Best overlapping cells are larger than Maximum Cell Size allowed.
Replace large cells by Maximum Cell Size and re-compute vectors
Vector Solver
Vector Solver
If
If
If
If
Take cells from zone below and compute new transition vector.
Update zone limits.
Geological features
  Cell size (> 0)
  Expansion factor (1.0 to 1.4)
  Maximum cell size
  Transition factor (default 1.4)
Final Mesh
Pre-processing
Remove small zones
Test if each zone can contain at least 5 cells.
Zone removed
The zone is merged to the neighboring zone with the smallest Cell Size.
Expansion factor 1.0
For every zone with an Expansion factor of 1.0, test is the zone depth can hold an integer number of cells.
Depth Adjusted
The lower boundary of the zone is adjusted for an integer number of cells for the specified Cell Size.
Fail
Fail
Pass
Pass
Maximum Cell Size
Check if the specified Maximum Cell Size is at least as large as the input cell size for the zone
Change Max Cell Size
Max Cell Size is changed to Cell Size
Fail
Pass
Easy Transition
Test if smallest Cell Size can transition to the next zone, leaving at least 3 cells in the host zone.
Change Cell Size
Cell Size of the host zone is adjusted.
Fail
Zone iteration
Vector Solver